## Slide 1
1D Strided Access → 2D Block I/O Reshape
MaterializeBlockPointer Optimization Intel XPU Backend for Triton
PR #6693 | April 2026
Notes: This presentation explains the 1D-to-2D block I/O reshape optimization added to the Intel XPU Backend for Triton. The optimization detects flattened 1D gather/scatter patterns produced by PyTorch Inductor and reshapes them into efficient 2D block load/store instructions, achieving 80%+ bandwidth improvement on PVC.

## Slide 2
The Problem: Inductor’s Flat 1D Scatter
# PyTorch Inductor flattens 2D tile
# access into 1D indexing:
col = xindex % W
row = xindex // W
addr = col + row * S
tl.store(out_ptr + addr, val, mask)
Memory (H=3, W=4, S=6):
addr: 0 1 2 3 [..] 6 7 8 9 [..]
|-- row 0 --|pad |-- row 1 --|pad
idx 0→0, 1→1, 2→2, 3→3
idx 4→6, 5→7, 6→8, 7→9
idx 8→12, 9→13, 10→14, 11→15
Result: N independent pointer computations → N scalar scatter/gather → N LSC messages
Performance Impact (Issue #6532)
Measured on PVC: 350 GB/s with scatter vs 818 GB/s with 2D block (+134%)
Pattern is ubiquitous: cat-fusion, attention stores, pointwise epilogues
Addresses ARE regular (row-major 2D) — compiler can’t see through arithmetic
1024 elements → 1024 scalar LSC messages (should be 1 block message)
Notes: PyTorch Inductor generates Triton kernels that store/load tensor slices using flattened 1D indexing for simplicity. This is the standard code pattern for cat-fusion, attention output stores, and pointwise epilogues.
The Triton compiler cannot see the underlying 2D regularity - it treats each address as independent. Each element becomes its own scatter/gather message to the LSC (Load Store Cache) unit.
Measured impact on PVC (Issue #6532): only 350 GB/s bandwidth vs 818 GB/s achievable - a 2.3x gap. This pattern is extremely common: any operator that writes a slice of a larger tensor (convolutions writing to padded output, concatenation, strided attention stores).
Key insight: the addresses ARE regular (row-major 2D tile) - the compiler just can't see it through the flattened arithmetic.

## Slide 3
The Solution: Recover 2D Structure via Pattern Matching
INPUT IR (1D — N=1024 elements)
%idx = tt.make_range {start=0, end=1024}
%rem = arith.remui %idx, 32 ← col = idx % W
%div = arith.divui %idx, 32 ← row = idx / W
%mul = arith.muli %div, 96 ← row * S
%off = arith.addi %rem, %mul ← col + row*S
tt.load/store (tt.addptr %base, %off)
↓ Pattern Match: Extract W=32, H=32, S=96
OUTPUT IR (2D — [32, 32] tile)
%ptr_2d = tt.reshape %ptr : [1024] → [32, 32]
tt.load/store %ptr_2d
{ ttig.block_io = "row_major",
ttig.block_io_stride = 96 }
LLVM → triton_gen.2Dblockload/store
(1 LSC message replaces 1024 scalar ops)
block_io_stride carries S (row stride) from pattern matching to LLVM lowering.
The original 1D pointers are reshaped away — without this attribute the lowering cannot recover the pitch. Also serves as the anchoring signal for loads.
HW Constraint Gates
Pitch ≥ 64 bytes
Pitch mod 16 = 0
W ≤ 32 (f16) / 16 (f32) / 64 (i8)
H/warps ≤ 32 (load) / 8 (store)
idx = tt.make_range(0, N)
Mask must be all-true
Pass: MaterializeBlockPointer
Lowering: LoadStoreOpToLLVM.cpp
1024 scalar messages → 1 block message. Same data, 1000x fewer instructions.
Notes: The pass lives in MaterializeBlockPointer.cpp - it already handles 2D block pointer materialization; the 1D reshape is an extension.
Pattern matching is structural: walks backward from tt.addptr through addi -> remui + muli(divui, S) - must be exactly this shape.
The isCanonicalLinearIndex() check ensures the base index is a simple sequential range (rejects scaled or permuted indices that would break mod/div semantics).
HW constraints come from Intel LSC 2D block I/O spec: pitch alignment, tile width limits per element type, height limits.
Once validated, the transformation is simple: tt.reshape the 1D tensor to 2D, annotate with ttig.block_io and ttig.block_io_stride.
The LLVM lowering (LoadStoreOpToLLVM.cpp) detects these annotations, bypasses normal tile-size heuristics, and uses the explicit stride as the pitch value.
Why block_io_stride? It carries the row stride S (in elements) from the pattern matching phase to the LLVM lowering phase. After the reshape, the original 1D pointer arithmetic is gone - the lowering cannot recover the pitch from pointer analysis. The attribute is the only way this information survives across passes. In the lowering: pitch = block_io_stride * elemSizeInBytes (e.g., 96 * 2 = 192 bytes for f16). It also doubles as the anchoring signal for loads - its presence tells isExpensiveLoadOrStore() to protect the ConvertLayoutOp from elimination.
End result: what was 1024 scalar messages becomes 1 hardware 2D block message - same data, dramatically fewer instructions.

## Slide 4
Load vs Store: The Encoding Challenge
Store Path (Simple)
tt.reshape [N] → [H, W]
tt.store { block_io = "row_major" }
✓ Done — HW accepts any register
order for writes
Load Path (Complex — PR #6693)
1. Build "load encoding" matching HW:
sizePerThread=[H/warps, 1]
threadsPerWarp=[1, 32]
warpsPerCTA=[numWarps, 1]
2. tt.reshape [N]→[H,W] (load enc)
3. tt.load { block_io, stride }
4. ttg.convert_layout ← ANCHORED
5. tt.reshape [H,W]→[N] (consumer)
Why? — HW delivers data in a fixed pattern that doesn’t match consumer layout
HW delivery (load enc): Consumer expects (1D blocked):
lane 0 → col 0, ALL rows thread 0 → elements [0..7]
lane 1 → col 1, ALL rows thread 1 → elements [8..15]
lane 2 → col 2, ALL rows thread 2 → elements [16..23]
... ...
→ ConvertLayoutOp (SLM transpose) bridges the mismatch
// Utility.cpp — isExpensiveLoadOrStore()
// Without anchoring: RemoveLayoutConversions
// eliminates ConvertLayoutOp → WRONG RESULTS
if (blockIOAttr && !has("ttig.block_io_stride"))
return false; // normal block IO: cheap
// 1D-reshaped loads: expensive → ANCHORED
Notes: STORES write data FROM registers TO memory. The 2D block store HW accepts data in whatever register order the GPU provides - it just writes the 2D tile. So reshaping the store input is sufficient.
LOADS deliver data FROM memory TO registers in a FIXED hardware pattern: subgroup lane k always receives column k, and successive registers contain successive rows. This is dictated by the LSC 2D block load microarchitecture.
The rest of the pipeline (consumers of the loaded value) expects the data in the original 1D blocked layout - e.g., sizePerThread=[8], threadsPerWarp=[32] means thread 0 owns elements 0-7, thread 1 owns 8-15, etc.
The HW delivery order is completely different: thread 0 owns column 0 of ALL rows, thread 1 owns column 1, etc.
A ConvertLayoutOp (which lowers to an SLM sub-group transpose) bridges between these two layouts.
CRITICAL CORRECTNESS POINT: The RemoveLayoutConversions pass aggressively eliminates 'unnecessary' layout conversions. Without anchoring, it would remove our ConvertLayoutOp, change the load's encoding to match consumers directly, and the 2D block load would deliver data in the wrong positions -> silent data corruption.
The anchoring mechanism: isExpensiveLoadOrStore() returns TRUE for ops with ttig.block_io_stride, which tells RemoveLayoutConversions 'this load's encoding is fixed - do NOT optimize it away'.
The SLM transpose cost is small (~few cycles) compared to the gain from replacing N scatter loads with 1 block load.

## Slide 5
Feature Evolution & Performance Results
Apr 7 PR #6531 Store reshape (initial)
Apr 16 PR #6682 Fix H>1 bug (restrict H=1)
Apr 17 PR #6695 H=1 test coverage
Apr 19 PR #6691 Refactor → reusable helpers
Apr 19 PR #6693 Load reshape (this PR)
PVC Bandwidth (Issue #6532)
Config | Before | After | Gain
W=32 S=96 f16 | 350 GB/s | 818 GB/s | +133%
W=32 S=128 f16 | 459 GB/s | 833 GB/s | +82%
W=32 S=96 f32 | 754 GB/s | 1330 GB/s | +76%
Average (9 cfg) |  |  | +81%
Current Status
Aspect | Store | Load (PR #6693)
Multi-row (H>1) | Disabled (HW transpose) | Supported via ConvertLayoutOp
Mask support | All-true only | All-true only
Encoding overhead | None | SLM transpose (~few cycles)
Max per-warp height | 8 | 32
Future Work
Fix H>1 for stores (per-warp offsetY in LLVM lowering)
Support non-trivial masks (partial tile loads/stores)
Extend pattern matching beyond exact Inductor idiom
Notes: The feature was built incrementally over 2 weeks - each PR addressed one concern cleanly.
PR #6531 (store): The initial implementation worked for the simple case but had a lurking bug - when H>1, the LLVM lowering hardcoded offsetY=0, putting all rows at the same Y coordinate.
PR #6682 (fix): Rather than rush a complex fix, the team restricted to H=1 (which covers the most common Inductor pattern: single-row slices into wide concatenated tensors).
PR #6693 (load): The load path is architecturally different - it introduces the 'load encoding + ConvertLayoutOp' pattern that correctly handles H>1 because each warp reads its own row slice, and the SLM transpose fixes ordering.
Performance context: The +81% average gain is on PVC (HBM memory). On GDDR6 (B580), the gains are smaller because the bottleneck shifts to DRAM row-buffer thrashing - a hardware limitation that no compiler trick can fix.
No regressions: PR #6693 was validated on Grafana CI benchmarks (Max 1550 + B580) with no performance regression.
Future work: (1) Fix H>1 for stores by computing per-warp offsetY in the LLVM lowering, (2) Support non-trivial masks, (3) Potentially extend pattern matching beyond the exact Inductor idiom.